## Slide 1: CER Electricity Pilot: Summary Information
Prepared by the sphynxes

## Slide 2: Pilot Basics
Goals
  Product identification – Best option
  Technical Learning – Rollout experience
  Risk identification/Assessment – Unforeseen challenges
Data Collection
  Business and residential demographics
  Different meter types
  Energy Usage
  User perceptions

## Slide 3: Pilot System Implementation
Stage 1: Design
Stage 2: Testing and Quality Assurance
Stage 3: Deployment, upgrades and enhancements of systems in the field
Stage 4: Measurement and Evaluation

## Slide 4: Stage 1: Design
Overall solution architecture
Functionality of the system
Communications performance model
Data model
Meter type and schema
Security architecture
Documentation and implementation plan.
User Manuals and system support

## Slide 5: Stage 2: Testing & Quality Assurance
Factory Unit Testing (Meters)—demonstrate that the meter meets the functional requirements
Factory System Testing (Full Metering System)—assure the functionality of the complete metering system
Sandbox System Integration Testing (Metering System)— tests were carried out prior to deployment of the system in a ‘Live Environment’ in ESB.
Field Soak Test (Metering System)—The soak test involves installing a small number of meters in a production environment and verifying that they operate correctly over a reasonable period of time. The intention is to identify any type faults before installing equipment on a big scale
Site acceptance, stress and volume testing (Metering System)

## Slide 6: Stage 3: Deployment, Upgrades, and Enhancements
Deployment Planning and Area selection—selection of the trial areas, positions and customer types.
Customer information—written communications with all customers in the trial areas and responding to their queries
Pilot Deployment—(i) to test ESB Networks deployment processes for different types of meters and the performance of different communication technologies on real networks; (ii) to identify problems before full deployment.
Communications models—predict performance and to identify the best places to locate communications devices.
Mass Deployment—Installation of the customer meters.
Upgrades / fixes for defects and issues discovered in the field.

## Slide 7: Stage 4: Measurement & Evaluation
During this phase the performance of the system in relation to the various functionalities was measured
3 Scenarios:
  Urban / Rural locations
  Overhead / underground network
  Indoor / Outdoor / Centralized Meter Position

## Slide 8: Survey Information
Pre- & post-experiment phone questionnaires given to both residential and business customers
Sought to identify:
  Baseline consumption patterns, perception of these patterns, household demographics
  Extent of efficiency efforts, openness to changing behavior
  Demand elasticity and knowledge of markets
Typical question formats: yes/no, agree/disagree on numerical scale, multiple choice

## Slide 9: Implementation Issues & Challenges
Statistical Concerns:
Potential selection bias
Control group/counterfactual
Participant attrition
Execution:
Daily collection of meter profile data
2.4GHz mesh performance in rural areas
3% of meter installations experienced technical difficulties
Electricity network conditions

## Slide 10: Relevant Literature
Results of Smart Meter Trials (2011)
2.5% avg. reduction in electricity demand for residential customers, with avg. peak usage reductions of 8.8%
82% of customers changed their electricity use
Smart Meters provide a net benefit to customers and the country of €175 million over the next 15-20 years
Results of Smart Meter Natural Gas Trials (2011)
2.9% avg. reduction in gas demand
A national rollout would reduce CO2 emissions by 1,167,000 tons and save the country €59 million over the next 20 years